## Slide 1: AI-Enabled Sensing and Controlling

## Slide 2: The Jist
AI-Enabled Sensing and Controlling refers to using artificial intelligence to perceive the environment (sensing) and make decisions/take actions (controlling) based on that perception.

## Slide 3: Sensing Component: Camera-Based Perception
What the Camera "Sees":
  Object Detection: Identifying and localizing vehicles, pedestrians, cyclists, traffic signs, lane markings
  Classification: Determining object types (car, truck, motorcycle, bus)
  Tracking: Following objects across frames to understand motion
  Depth Estimation: Understanding distance to objects (monocular or stereo cameras)
  Segmentation: Pixel-level understanding of drivable areas, obstacles, sky, etc.

## Slide 4: Sensing Component: Camera-Based Perception
AI Models Used:
  Convolutional Neural Networks (CNNs):
    Extract visual features from camera images
    YOLOv3, Faster R-CNN, MobileNet for object detection
    Process images at 30+ FPS for real-time operation
  Multi-Task Networks:
    Simultaneously detect objects, lanes, and traffic signs
    Efficient for embedded automotive hardware
  Temporal Models (RNNs/Transformers):
    Track objects across video frames
    Predict future trajectories

## Slide 5: Sensing Component: Camera-Based Perception
Key Advantages:
  Cost-effective: Cameras are cheaper than LiDAR
  Rich information: Color, texture, text on signs
  Proven technology: Mature computer vision algorithms
  Passive sensing: No active emissions needed
Challenges:
  Weather sensitivity: Rain, fog, glare affect performance
  Lighting conditions: Shadows, night driving, backlighting
  Depth ambiguity: Harder to judge exact distances than LiDAR
  Adversarial vulnerability: Susceptible to attacks

## Slide 6: Controlling Component: Decision Making & Actuation
Perception to Action Pipeline:
  Camera → AI Detection → Scene Understanding → Decision Logic → Vehicle Control
1. Scene Understanding:
  Fuse detections from multiple cameras (360° coverage)
  Build occupancy grid or semantic map
  Identify critical objects (e.g., vehicles in collision path)
2. Decision Making:
  Path Planning: Determine safe trajectory
  Behavior Planning: Decide to slow down, change lanes, stop
  Threat Assessment: Prioritize objects by collision risk
  Rule Compliance: Follow traffic laws
3. Control Execution:
  Longitudinal Control: Acceleration/braking
  Lateral Control: Steering adjustments
  Emergency Response: Automatic emergency braking (AEB)

## Slide 7: Controlling Component: Decision Making & Actuation
AI Control Strategies:
  Rule-Based Control:
    If vehicle detected < 10m ahead → Apply brakes
    If lane marking crossed → Steer back
    Transparent, verifiable, but limited flexibility
  Learning-Based Control:
    Imitation Learning: Learn from human drivers
    Reinforcement Learning: Optimize driving policies
    End-to-End Learning: Direct camera-to-control mapping
    More adaptive but harder to validate for safety
  Hybrid Approaches (Most Common):
    AI for perception and prediction
    Validated algorithms for control
    Human-interpretable decision logic

## Slide 8: Real-World Applications
ADAS (Advanced Driver Assistance Systems):
Adaptive Cruise Control (ACC):
  Camera detects lead vehicle
  Maintains safe following distance
  Adjusts speed automatically
Automatic Emergency Braking (AEB):
  Detects imminent collision
  Warns driver, then brakes if no response
  Critical safety feature in modern vehicles
Lane Keeping Assist (LKA):
  Cameras detect lane markings
  Gently steers to keep vehicle centered
  Prevents unintentional lane departure
Blind Spot Detection:
  Side cameras monitor adjacent lanes
  Alerts driver to vehicles in blind spots
  Traffic Sign Recognition:
  Reads speed limits, stop signs, yield signs
  Displays to driver or adjusts cruise control
Autonomous Driving Levels:
  Level 2 (Tesla Autopilot, GM Super Cruise): Camera-based partial automation
  Level 3+: Cameras + LiDAR + Radar for redundancy
  Tesla's Approach: Camera-only "vision" system(controversial in industry)

## Slide 9: System Architecture Example

## Slide 10: How LiDAR Lets Robots “See” the World
From Raw Data to Intelligence.
What is LiDAR?
Stands for Light Detection and Ranging.
ToF (Time of Flight) Principle: The sensor emits a laser pulse and measures the time it takes to bounce back.
Formula: (where is the speed of light).
The Advantage:
Active Sensing: Works in total darkness (unlike cameras).
Direct Depth: Provides centimeter-level 3D geometry immediately.
Real-world Use: The backbone of Self-Driving Cars, Warehouse Robots (AGVs), and Drones.

## Slide 11: Data Representation: The Point Cloud
From Beams to Points.
The "Point Cloud":
The output isn't a photo; it’s a collection of coordinates.
It represents the physical skeleton of the world.
Critical Concepts:
Occlusion: LiDAR cannot see through walls—it creates "shadows" behind objects.
Sparsity: The further the object, the fewer points we collect.

## Slide 12: Hands-on Simulation — Building the LiDAR Engine
1. Environment Modeling (The "Digital Twin")
Virtual Space: A 2D coordinate system representing an 18 x 18 warehouse.
Dynamic Obstacles: Randomized generation of polygonal obstacles
using the shapely library to mimic real-world hazards like crates or pillars.
2. The Ray Casting Engine
360° Scanning: Simulating a hardware sensor by firing 360 virtual laser beams (1 beam per degree).
Geometric Intersection: Using shapely.geometry to calculate exact mathematical intersections between laser rays and obstacle boundaries.
Range Extraction: Determining the precise distance by identifying the nearest intersection point for each beam.
Notes: In this notebook, we move from hardware concepts to software implementation. As you run the code, notice the 'Occlusion' effect: the LiDAR cannot see behind obstacles, creating blind spots (shadows). This raw geometric data — the Green Dots — is the foundation of our next two modules:
Part 2 — Obstacle Awareness
These LiDAR points illustrate how autonomous systems identify geometry, detect obstacles, and reason about free space.
Part 3 — Reinforcement Learning (Conceptual Bridge)
In real autonomous systems, LiDAR data can be converted into state representations for AI-driven navigation.
In our workshop, we will simulate this idea using a training environment where the agent learns to avoid collisions through trial-and-error.

## Slide 13: Turning LiDAR Data into Perception & Planning
From Sensing to Intelligence.
Sense: Capture raw LiDAR distances (The Green Dots)
Think: Identify obstacles and "Safe Zones.
Act: Calculate steering and speed.
Moving from "What is around me?" to "What should I do?

## Slide 14: Turning LiDAR Data into Perception & Planning
From Sensing to Intelligence.
Moving from "What is around me?" to "What should I do?
AI use perception to support:
Short-term reactions: avoiding collisions
Mid-term planning: deciding where to move next
Long-term goals: reaching destinations safely

## Slide 15: Why LiDAR Perception is Foundational
From Sensing to Intelligence.
Moving from "What is around me?" to "What should I do?
Enables safe autonomy
Supports navigation
Forms the base for:
Obstacle avoidance
Path planning
And eventually… Reinforcement Learning control

## Slide 16: Deep Reinforcement Learning for Autonomous Driving
Perception → Planning/Decision → Control
↑ ↑ ↑
Completed This Session Execution
What We Covered:
How LiDAR captures 3D point cloud data
How to detect vehicles, pedestrians, obstacles from point clouds
Output: position, velocity, and class of surrounding objects

## Slide 17: From Perception to Decision Input
The Decision Module Must Answer:
Should I change lanes?
Speed up or slow down?
When to overtake?
Core Challenge: How to convert perception data into driving actions?

## Slide 18: From Perception to Decision Input
What is Reinforcement Learning?
Core Idea: Learn optimal decisions through trial and error
Similar to How Humans Learn to Drive:
Beginner: Doesn't know when to change lanes
Tries changing lanes → Nearly crashes (negative feedback) → Learns to check mirrors first
Practice repeatedly → Develops driving intuition

## Slide 19: From Perception to Decision Input